## Slide 1: Smart lock
An Android device for controlling and monitoring purpose

## Slide 2: system architecture
Smartphone
Android Device
Any phone
Controller
Remote device

## Slide 3: Use cases
Start.
Incoming Bluetooth connection.
Incoming SMS.
Incoming Call.
Incoming Connection over Internet.

## Slide 4: Hardware section

## Slide 5: Serial communication
RS232:a Serial port with 9 pins.
MAX232:adapt the RS-232 signal voltage levels to TTL logic, it just needs one voltage (+5V) and generates the necessary RS-232 voltage levels (approx. -10V and +10V) internally.
Converter: A USB-to-RS232 cable.

## Slide 6: Sensors
LDR is sensitive to light.
Temperature Sensor (LM335): analog sensitive to heat .
Gas Sensor (MQ-5): sensitive to gas, especially methane and propane.

## Slide 7: Controller
ATMEGA16A 40 pin:
  32 I/O pins:
    2 pins for Serial communication (TX,RX)
  8 ADC pins:
    10 bit Resolution.

## Slide 8: Terminals
Motor: 5V DC motor to simulate a garage door
  Pulse width modulation.
  H-Bridge Circuit.
Relay: an electrically operated switch which operates a switching mechanism mechanically.

## Slide 9: Android user interface application

## Slide 10: Application responsibilities
This application control the android lock

## Slide 11: Turn on Bluetooth
The application ask the user To turn on Bluetooth
and Make the device discoverable

## Slide 12: Connect with android device
The application ask the user To pair with android device

## Slide 13: Mechanism of the application
Control Via Bluetooth
Via SMS

## Slide 14: Make a call
The application call the android device